## Slide 1: Introduction to OSPF
Campus Networking Workshop
These materials are licensed under the Creative Commons Attribution-Noncommercial 3.0 Unported license (http://creativecommons.org/licenses/by-nc/3.0/)
Campus Networking Workshop
Introduction to Cisco Router Configuration

## Slide 2: Cisco router components: Memory types
RAM: Stores packet buffers, ARP cache, routing table, software code and data structures necessary for router operation. Running configuration and decompressed IOS code is stored in RAM
ROM: Contains basic software for hardware testing and initialization.
Flash: Stores IOS and backup configuration files. Not volatile.
NVRAM (non-volatile RAM): Saves router configuration.

## Slide 3: Cisco router components: Sofware
POST: Power-on Self-Test. Stored in ROM. Checks basic router functions
Bootstrap: In ROM. Initiates router and loads IOS
ROM Monitor: In ROM: Used for tests and troubleshooting. Basic interface for troubleshooting low-level issues.
IOS (Internetwork Operating System): Provides all of the higher-level router functionalities

## Slide 4: Configuration Register
config-register
Controls various low-level settings
  Tell router to load or ignore configuration
  Terminal behavior
Current value can bee seen with show version
Most common settings are:
  0x2102 – Normal
  0x2142 – Ignore configuration

## Slide 5: Where is the configuration?
Router always has two configurations
  running-config
    In RAM. Shows which parameters are currently in use.
    Modified with configure terminal command
    show running-config
  startup-config
    In NVRAM. Loaded by router in next reboot
    This is where the running-config is saved
    show startup-config

## Slide 6: Configuration backups
You can store configuration in other places
  In router’s Flash memory
  In a server, via TFTP
Can be copied around with copy command
  copy running-config startup-config
  copy running-config tftp
  copy startup-config tftp
  copy startup-config flash:saved-config
  copy flash:saved-config startup-config

## Slide 7: Access Modes
User EXEC
  Limited access. Show router state, etc.
    Router>
Privileged EXEC (enabled mode)
  Detailed examination, manipulate configuration and files, run tests, debugging, etc.
    Router#
ROM Monitor
  Password recovery and IOS installation

## Slide 8: Management input sources
Console: Direct access via serial port
Auxiliar Port: Access via Modem
Virtual Terminals (VTY): Telnet/SSH

## Slide 9: Changing the configuration
Commands are activated immediately
  Be careful when typing!
When working on serial console or via Telnet or SSH, commands can be copied from a text file and pasted into the terminal

## Slide 10: Changing the configuration
  router>
  router>enable
  [type password]
  router#
  router# configure terminal
  router(config)#
  [type commands]
  router(config)# end
  router# write memory

## Slide 11: How to tell where you are
  Router> - USER EXEC
  Router# - PRVILEDGED EXEC
  Router(config) – Global configuration
  Router(config-if) – Interface configuration
  Router(config-subif) – Sub-interface configuration
  Router(config-route-map) – Route-map configuration
  Router(config-router) – Routing protocol configuration
  Router(config-line) – Line configuration
  rommon 1> - ROM Monitor

## Slide 12: Context Help
Use “?” to obtain a list of commands available in your current configuration mode
Router(config)#?
Configure commands:
aaa Authentication, Authorization and Accounting.
aal2-profile Configure AAL2 profile
access-list Add an access list entry
alarm-interface Configure a specific Alarm Interface Card
alias Create command alias
appfw Configure the Application Firewall policy
application Define application
archive Archive the configuration
arp Set a static ARP entry

## Slide 13: Online help
Use “?” also to see all possible parameters to an incomplete command:
Router(config)#username ?
WORD User name
Router#show ?
aaa Show AAA values
aal2 Show commands for AAL2
access-expression List access expression
access-lists List access lists
accounting Accounting data for active sessions

## Slide 14: Command completion
Use the Tab key to complete a command
  router(config)#int<TAB>
  router(config)#interface et<TAB>
  router(config)#interface ethernet 0
  router(config-if)#ip add<TAB>
  router(config-if)#ip address n.n.n.n m.m.m.m

## Slide 15: Moving faster around the command line
Move within command history
     Previous command
     Next command
Line editing
   and  to move within the line
  Ctr-a move to beginning of line
  Ctrl-e move to end of line
  Ctrl-k delete until end of line

## Slide 16: Verifying and troubleshooting
show running-config
show run interface f0/0
show ip int brief
debug ip ospf hello / events / adj
show log
show version