## Slide 1: VPN: Virtual Private Networks
Presented by:
MICHELLE OPIYO
Transforming education through ICT

## Slide 2: INTRODUCTION
Transforming education through ICT
What is a VPN?

## Slide 3: Introduction: What is a VPN?
Transforming education through ICT
Virtual
Private
Network

## Slide 4: INTRODUCTION TO VPN
Transforming education through ICT
A VPN is a private network in the sense that it carries confidential information, protected by various security mechanisms, between known parties.
VPNs are only "virtually" private, because the data actually travels over shared – open to all public internet networks instead of fully dedicated private connections. E.g: private leased line

## Slide 5: Introduction to VPN
Transforming education through ICT

## Slide 6: Closed Private Networks vs. Virtual Private Networks
Transforming education through ICT
*Closed Private Networks : - private leased lines, private Intranet links [fiber/copper …]
VPN - The public Internet is used as the backbone for VPNs. This saves costs tremendously from reduction of equipment and maintenance, leased line costs

## Slide 7: VPN TOPOLOGY
Transforming education through ICT
How does a VPN work?

## Slide 8: VPN Topology: Types of VPNs
Transforming education through ICT
Remote access VPN
Intranet VPN
Extranet VPN

## Slide 9
Transforming education through ICT
Remote Access/ Road Warrior VPN – Allows constantly moving employees to securely connect to office. A VPN client is normally required. All user needs is credentials – VPN config “pushed” to user
Intranet – Connects remote branches of the organization to the hub/hq
Extranet – Provide business partners, sub-contractors secure access to critical internal data

## Slide 10: VPN Topology: Remote Access VPN
Transforming education through ICT

## Slide 11: VPN Topology: Intranet VPN
Transforming education through ICT

## Slide 12: VPN Topology: Extranet VPN
Transforming education through ICT

## Slide 13: VPN Topology: Advantages and Disadvantages of VPN
Transforming education through ICT
Advantages:
  Greater scalability
  Easy to add/remove users
  Reduced long-distance telecommunications costs
  Mobility
  Security

## Slide 14: VPN Topology: Advantages and Disadvantages of VPN
Transforming education through ICT
Disadvantages
  Lack of standards
  Understanding of security issues
  Unpredictable Internet traffic
  Difficult to accommodate products from different vendors

## Slide 15: VPN Topology: What is needed?
Transforming education through ICT
Existing hardware (Servers, workstations,…)
Internet connection
VPN - Router/Switch
Software to create and manage tunnels
Security Device such as firewall

## Slide 16: VPN Topology: How it works
Transforming education through ICT
Operates at layer 2 or 3 of OSI model
  Layer 2 frame – Ethernet
  Layer 3 packet – IP
Tunneling
  allows senders to encapsulate their data in IP packets that hide the routing and switching infrastructure of the Internet
  to ensure data security against unwanted viewers, or hackers.

## Slide 17: VPN COMPONENTS
Transforming education through ICT
What are the components of VPN?

## Slide 18: VPN Components
Transforming education through ICT
Protocols
Security
Appliances

## Slide 19: VPN Components: Protocols
Transforming education through ICT
IP Security (IPSec)
  Transport mode
  Tunnel mode
Point-to-Point Tunneling Protocol (PPTP)
  Voluntary tunneling method
  Uses PPP (Point-to-Point Protocol)

## Slide 20: VPN Components: Protocols
Transforming education through ICT
IP Security (IPSec)
  Transport mode
  Tunnel mode
Point-to-Point Tunneling Protocol (PPTP)
  Voluntary tunneling method
  Uses PPP (Point-to-Point Protocol)

## Slide 21: VPN Components: Protocols
Transforming education through ICT
Layer 2 Tunneling Protocol (L2TP)
  Exists at the data link layer of OSI
  Composed from PPTP and L2F (Layer 2 Forwarding)
  Compulsory tunneling method

## Slide 22: Example of packet encapsulation
Transforming education through ICT

## Slide 23: VPN Components: Security
Transforming education through ICT
Encryption
  Technique for scrambling and unscrambling information
  Unscramble – called clear-text
  Scrambled information – cipher-text

## Slide 24: VPN Components: Security
Transforming education through ICT
Keys
  Secret code that the encryption algorithm uses to create a unique version of cipher-text
  8-bits keys = 256 combinations or two to the eighth power
  16-bits keys = 65,536 combinations or two to the 16th power
  56-bits keys = 72,057,594,037,927,900 or two to the 56th power
  168-bits keys …

## Slide 25: VPN Components: Security
Transforming education through ICT
TYPES OF ENCRYPTIONS
SYMMETRIC ENCRYPTIONS
Sender, receiver share the secret key. In communications with each other the secret key is used to encrypt, decrypt data

## Slide 26: VPN Components: Security
Transforming education through ICT
ASSYMETRIC ENCRYPTION
Public Key encryption
Each of the parties involved has crypto two keys. A public key known to all and a private key known only to owner
A wants to communicate with B. A looks up B’s public key and uses it to encrypt data. The encrypted data can only be decrypted using B’s private key

## Slide 27: VPN Components: Security
Transforming education through ICT
Digital Signatures:
B wants to communicate with A – needs to confirm A’s id. To authenticate himself, A signs a message using his private key to generate digital signature. B takes encrypted message, A’s public key and runs signature verification to confirm authenticity

## Slide 28: VPN Components: Security
Transforming education through ICT
Authentication
  Determine if the sender is the authorized person and if the data has been redirect or corrupted
  User/System Authentication
  Data Authentication

## Slide 29: VPN Components: Appliances
Transforming education through ICT
Intrusion detection firewalls
  Monitors traffic crossing network parameters and protects enterprises from unauthorized access
  Packet-level firewall checks source and destination
  Application-level firewall acts as a host computer between the organization’s network and the Internet

## Slide 30: QUALITY OF SERVICE (QoS)
Transforming education through ICT
WHAT IS QoS?

## Slide 31: What is QoS?
Transforming education through ICT

## Slide 32: VPN Productivity and Cost Benefits: Quality of Service
Transforming education through ICT
Question: “Do I get acceptable response times when I access my mission critical applications from a remote office?”

## Slide 33: QoS Options
Transforming education through ICT
Two models are available for QoS functionality:
  Differentiated Services Model (DiffServ)
  Integrated Services Model (IntServ)

## Slide 34: Differentiated Services Model (DiffServ)
Transforming education through ICT

## Slide 35: Integrated Services Model (IntServ)
Transforming education through ICT

## Slide 36: QUESTIONS?
Transforming education through ICT

## Slide 37: Thank You
www.kenet.or.ke
Jomo Kenyatta Memorial
Library, University of Nairobi
P. O Box 30244-00100, Nairobi.
0732 150 500 / 0703 044 500