## Slide 1
Security Landscape in IPv4 and IPv6
Transforming Learning, Research and Working Environments using ICT
STRENGTHENING KENYA'S CYBERSECURITY POSTURE

## Slide 2: Training Objectives
Transforming Learning, Research and Working Environments using ICT
By the end of this session, you will: ✔ Identify critical IPv4 vulnerabilities (NAT, DHCP spoofing). ✔ Understand IPv6-specific threats (NDP spoofing, rogue RA). ✔ Apply mitigation strategies for hybrid (IPv4/IPv6) networks.

## Slide 3: IPv4 Security Overview
Transforming Learning, Research and Working Environments using ICT
Widely deployed but originally not designed with security in mind
Relies on NAT and stateful firewalls for basic protection
Still vulnerable to multiple Layer 2 and Layer 3 threats
Notes: Internet when it began was for the academic and research community before it was commercialised. The community was trusted and the focus was in communication
Stateful firewall maintains a state table that stores information on every current connection coming through it and blocks unsolicited replies
ACLs on routers/firewalls useful in to inspect IPv4 traffic
While NAT was primarily to address IPv4 address exhaution, it has a form of security.blocks unsolicited inbound connections. Traffic dropped if no internal host requested connection.Nat hides internal structure of the private network

## Slide 4: IPv4 Vulnerabilities
Transforming Learning, Research and Working Environments using ICT
Legacy Risks Still Haunting Networks:
NAT Limitations:
NAT hides internal IPs but creates single points of failure
.
NAT also makes it difficult to find infected machines as they hide behind one IP address
Risk: State exhaustion attacks (results in DoS).
2. DHCP Spoofing:
Attackers impersonate DHCP servers to redirect traffic.
Impact: Data interception (e.g., student login theft).
Notes: NAT device can experience hardware failure-power, bug in OS, h/w defect. This effectively halts all communciation instantly
NAT device can have performance bottleneck- if there is more traffic that the CPU and memory that can be handled performance degrades for everyone
There can be failure in the translation table – the state table is finite and can be filled up and therefore no new entries for new connections and therefore DoS results
DHCP Spoofing – rogue DHCP servers can result in MITM attacks (attackers inspect , log,modify traffic before forwading to real router) DOS can also result if client issued with invalid/incorrect address or fake default gateway. User can not communicate with the rest of network. DNS redirection to phising sites by malicious DNS servers

## Slide 5: Demo – DHCP Spoofing in Action
Transforming Learning, Research and Working Environments using ICT
Video:
https://www.youtube.com/shorts/j14Qy2hpW9k
Steps:
Attacker sends fake DHCP offers
Devices connect to rogue gateway.
Traffic redirected to malicious DNS

## Slide 6: IPv6 Security Overview
Transforming Learning, Research and Working Environments using ICT
• Built-in security features like IPSec (optional, not always implemented)
• Larger address space reduces scanning risk
IPv4-4.3B addresses: Low-effort, automated, wide-scale scanning quickly
IPv6 –2^128 addresses: Automated wide-scale scanning is futile.
• Stateless Address Autoconfiguration (SLAAC) introduces new risks (RA and NDP spoofing)
:
Notes: Despite the original intent to mandate IPsec, the standard was eventually softened, and its use became optional in many real-world IPv6 deployments because of performance and processing overheads as well as backward compatibity and interoperability(For seamless network operation, all devices need to agree on and correctly implement the same IPsec policies, keys, and algorithms). It is notable that Most internet communication today is already secured by layers above the network layer like the VPNS as well as TLS
Even with the fastest modern scanning tools, checking every address in a single $/64$ subnet would take millions of years. Also, Because the IPv6 address space is so large, administrators do not need to use addresses sequentially it can be random

## Slide 7: IPv6 Threats – New Challenges
Transforming Learning, Research and Working Environments using ICT
IPv6 Solves Old Problems, Introduces New Ones
NDP Spoofing:
Fake Neighbor Advertisements poison caches.
Result: Man-in-the-middle (MITM) attacks.
2. Rogue Router Advertisements (RA):
Advertise fake default gateways
Cause routing confusion or DoS
Redirect traffic
3. Tunneling Attacks
Attackers encapsulate IPv6 in IPv4 (e.g., 6to4, ).
Bypasses firewalls.
:
Notes: Tunneling Attacks- these attacks use legitimate tunneling mechanisms designed for transition to carry malicious IPv6 traffic over an IPv4-only infrastructure, bypassing security checks that only inspect IPv4 traffic.

## Slide 8
Transforming Learning, Research and Working Environments using ICT
Threat Type | IPv4 | IPv6
Spoofing | DHCP Spoofing | NDP Spoofing
Gateway Attacks | ARP Poisoning | Rogue RA
Flood Attacks | SYN Floods | ICMPv6 Floods
Side-by-Side Comparison
Notes: Spoofing - rogue device impersonating a trusted network service to deliver false configuration data to clients.(gain control over trusted services identity)
Gateway attacks – MITM attacks (intercept all traffic destined outside network)
Flood attacks – DoS attacks

## Slide 9: Dual Stack Dangers
Transforming Learning, Research and Working Environments using ICT
Top Attack surfaces:
IPv6-enabled by default on modern OS → Unmonitored traffic
Asymmetric routing: IPv4/6 paths differ → Bypasses controls
DNS inconsistencies: A vs. AAAA record poisoning
Notes: unintentional exposure of systems and the increase in the network's attack surface.
Many legacy security tools, such as older firewalls, Intrusion Detection Systems (IDS), and Network Access Control (NAC) systems, were designed only to inspect IPv4 traffic.
Assymetric routing - dual-stack host or router manages two entirely separate routing tables; that directs IPv4 traffic one way and and IPv6 traffic a different way
DNS-Managing two sets of records introduces opportunities for human error and synchronization failures

## Slide 10: Best Practices & Mitigation Strategies
Transforming Learning, Research and Working Environments using ICT
IPv4
Rate-limit NAT translations
Isolate legacy IPv4-only devices
Implement DHCP snooping
Use Dynamic ARP Inspection
IPv6
Disable unused transition mechanisms (6to4)
Deploy RA Guard on switches
Use NDP Monitoring
Dual – Stack
Synchronize ACLs for both protocols
Monitor IPv6 flow logs (often ignored!)
General Network Segmentation
Train administrators regularly
Notes: control the rate and number of new NAT sessions that a device is allowed to create within a given time period.
Legacy IPv4-only devices are inherently unaware of IPv6 protocols and security. This isolation is a crucial security measure because these devices represent the weakest link in a modern dual-stack or IPv6 network infrastructure.
DHCP snooping is a security feature deployed on network switches that filters untrusted DHCP messages and builds a database of legitimate IP-to-MAC address bindings.
RA guard- Before you can apply RA Guard to individual ports, you must first enable the underlying IPv6 packet inspection features globally on the switch.
Monitoring IPv6 flow logs ensures that you have visibility into all network communication, allowing you to detect unauthorized IPv6 tunnels,

## Slide 11: Q & A
Transforming Learning, Research and Working Environments using ICT
Challenges in transitioning to or securing IPv6 ?

## Slide 12
www.kenet.or.ke
Jomo Kenyatta Memorial
Library, University of Nairobi
P. O Box 30244-00100, Nairobi.
0732 150 500 / 0703 044 500
Thank You