## Slide 1
Transitioning to IPv6 –Strategy and Security Considerations
Transforming Learning, Research and Working Environments using ICT
STRENGTHENING KENYA'S CYBERSECURITY POSTURE

## Slide 2: Objectives
Transforming Learning, Research and Working Environments using ICT
Understand IPv6 migration strategies (dual-stack, tunneling, translation).
Learn IPv6 security best practices (IPsec, NDP protection, firewall rules).
Examine case studies/experiences of IPv6 deployment in our institutions.
Basic hands-on tools to validate transition

## Slide 3: Why IPv6 now?
Transforming Learning, Research and Working Environments using ICT
IPv4 address exhaustion
Growing digital infrastructure needs(IoT and mobile devices)
Enhanced security and performance in IPv6

## Slide 4: IPv6 Migration Strategies
Transforming Learning, Research and Working Environments using ICT
1. Dual-Stack Approach
Run IPv4 and IPv6 simultaneously
Gradual transition, flexibility, increased overheads,processing power
2. Tunneling (6in4, 6to4)
Encapsulate IPv6 in IPv4 for compatibility,
3. Translation (NAT64/DNS64)
Allows IPv6-only clients to access IPv4 resources
Best Practices:
Assess network readiness
Update firewall rules
Train IT staff
Notes: Dual stack – +ves: no hard cut over, gradual migration, more flexibility. -ves: increased overheads-memory, processing power
Tunneling - ncapsulates IPv6 packets in IPv4 packets for delivery across an IPv4 infrastructure. can communicate with isolated IPv6 networks without upgrading the IPv4 infrastructure between them
Translations- provide seamless, transparent outbound connectivity from an IPv6-only network to the IPv4 Internet.WKP

## Slide 5: Securing IPv6 – Critical Actions
Transforming Learning, Research and Working Environments using ICT
4. Pro Tip:
Audit regularly: Many networks accidentally leave IPv6 unsecured—test and monitor! Disable unused IPv6 features
1. Core Principle
"Same-or-Better Rule" "IPv6 security ≥ IPv4 security"
2. Top IPv6 Threats
NDP Spoofing → Fake routers
Rogue SLAAC → Fake addresses
Header Exploits → DoS/Evasion
3. Must - Implement Controls Threat | Solution
Rogue Router Ads | ✅ RA Guard (on switches)
Fake DHCPv6 Servers | ✅ DHCPv6 Snooping
IPv6 Blind Spots | ✅ Dual-Stack ACLs (IPv4+IPv6)
Notes: Any security measure you have for IPv4 (e.g., firewalls, access control lists, intrusion detection) must be replicated for IPv6, or better
Ipv6 uses NDP on same LAN to discover each other, however has inherent vulnerability because in its original design, it lacks mechanisms to authenticate the source of its messages.
the flexibility and required processing of IPv6 headers can be a DOS concern
RA guard and DHCP snooping configured on layer 2 to secure gainst rogue attacks
SLAACautomatically configure its own unique, routable IPv6 address without needing a stateful server

## Slide 6: IPv6 Built-in Security – IPsec & Encryption
Transforming Learning, Research and Working Environments using ICT
1. IPsec in IPv6
🔒 Native (not add-on like IPv4)
Purpose: Encrypts + authenticates all IP traffic.
4. Why It Matters
✅ No extra cost (built into IPv6).
✅ Secures BYOD/cloud traffic in universities/TVETs.
2. Key Components Component | Role
AH 🏷️ | Integrity – Detects tampering.
ESP 🔐 | Encryption + Integrity (Most used).
3. Modes of Operation
Transport Mode 🖥️→🖥️: Encrypts only payload (e.g., host-to-host).
Tunnel Mode 🌐→🌐: Encrypts entire packet (e.g., site-to-site VPN).
Notes: IPSec is a suite of protocols that provides authentication and encryption at the IP layer
Transport mode - provides security for communication between two endpoints (host-to-host), where both devices are capable of running IPsec
Tunnel Mode provides security for communication between security gateways.
For securing traffic between hosts that are separated by the public Internet and/or NAT devices, IPsec Tunnel Mode is the required solution

## Slide 7: Leveraging IPsec for Secure Deployment
Transforming Learning, Research and Working Environments using ICT
Why IPsec? 🔐
Confidentiality: Encrypts sensitive data (research/admin).
Integrity: Ensures packets aren’t altered.
Authentication: Verifies sender identity.
Practical Use Cases 🏛️→🏛️
Inter-Campus Links
  Secure tunnels between universities (NREN backbone).
Server Protection
  Encrypts critical server-client traffic (e.g., student records).
Remote Access VPNs
  Safe access for staff/researchers (work-from-anywhere).
Action Item ✅
Audit your network

## Slide 8: Case Studies – Secure IPv6 in Education
Transforming Learning, Research and Working Environments using ICT
Leading the Transition locally
University (UoN/DeKUT)
Nyeri Polytechnic
Leading Transition Globally
Virginia Tech University started early,built a parallel network alongside IPv4,becoming one of the top IPv6 deployments globally in the education sector.
https://www.arin.net/vault/blog/2018/12/07/an-ipv6-journey-two-decades-in-the-making/
Your Turn! 💡
Is your institution IPv6-ready?
✅ Yes (testing phase) ❌ No (planning stage) 🔄 Partial deployment

## Slide 9: Critical Success Factors
Transforming Learning, Research and Working Environments using ICT
Start with a dual-stack core: Transition the backbone network first.
Address Planning is Key: A hierarchical, logical IPv6 address plan is critical for future growth and management.
Leverage Vendor Support: Work with hardware and software vendors to ensure IPv6 compatibility from the start.
Capacity Building: The most successful transitions involved dedicated training for network and security teams. This is a critical point that brings this training to life.

## Slide 10: IPv4 vs IPv6 Connectivity Testing
Transforming Learning, Research and Working Environments using ICT
🔄 Ping Comparison IPv4 | IPv6
ping -4 google.com | ping -6 google.com
Tests basic IPv4 reachability | Verifies IPv6 connectivity
🔍DNS Lookup (Dig) IPv4 Record | IPv6 Record
dig A google.com | dig AAAA google.com
Shows IPv4 addresses | Reveals IPv6 availability
🛡️Service Scanning (Nmap) IPv4 Scan | IPv6 Scan
nmap -sV 192.0.2.1 | nmap -sV -6 2001:db8::192:0:2:1/64
Checks IPv4 open ports | Tests IPv6 firewall rules
Notes: Nslookup
nslookup -querytype=AAAA google.com
https://nmap.org/download#windows

## Slide 11: Hands on Lab
Transforming Learning, Research and Working Environments using ICT
Exercise 1 : Ping Test 🛠️
Exercise 2 : DNS Check 🔍
Exercise 3 : Security scan 🛡️
only scan your own devices

## Slide 12: Q & A
Transforming Learning, Research and Working Environments using ICT
If the MOE mandated IPv6-only networks by 2030, what 3 steps would your institution need to take?

## Slide 13
www.kenet.or.ke
Jomo Kenyatta Memorial
Library, University of Nairobi
P. O Box 30244-00100, Nairobi.
0732 150 500 / 0703 044 500
Thank You