## Slide 1
Transforming Learning, Research and Working Environments using ICT
IP Addressing

## Slide 2: IP Addresses
Transforming Learning, Research and Working Environments using ICT
Internet connected networks use two types of IP Addressing
IPv4 – legacy Internet protocol
IPv6 – new Internet protocol
Presentation describes IPv4 addresses and IPv6 addresses & addressing
The Campus Network Design Workshop labs use both IPv4 and IPv6 for all exercises
Dual stack network (both protocols running in parallel)

## Slide 3: IPv4 Addresses
Transforming Learning, Research and Working Environments using ICT
•
32-bit binary number
– How many unique addresses in total?

## Slide 4: IPv4 Addresses
Transforming Learning, Research and Working Environments using ICT
32-bit binary number
How many unique addresses in total?
232 which is 4,294,967,296 addresses
Conventionally represented as four dotted decimal octets.
If you turn on all bits this is:
11111111111111111111111111111111
255 . 255 . 255 . 255
Can you explain why 11111111 = 255 in decimal?

## Slide 5: IPv4 Addresses
Transforming Learning, Research and Working Environments using ICT
•
•
Remember binary mathematics!
Each bit is basically to the power of 2. First bit is 20, second bit is 21 and so on to the eighth bit which is 27.
•
•
•
This means that :
11111111 = 20*1+21*1+22*1+23*1+24*1+25*1+26*1+27*1
11111111 = 1+2+4+8+16+32+64+128 = 255
2726252423222120
11111111

## Slide 6: IPv4 Addresses
Transforming Learning, Research and Working Environments using ICT
•
•
32-bit binary number
Conventionally represented as four dotted decimal octets
10000000110111111001110100010011
128 . 223 . 157 . 19
Can you explain why 00010011 = 19 in decimal?

## Slide 7: IPv4 Addresses
Transforming Learning, Research and Working Environments using ICT
•
•
•
•
00010011 = 20*1+21*1+22*0+23*0+24*1+25*0+26*0+27*0
00010011 = 1+2+0+0+16+0+0+0 = 19
32-bit binary number
Conventionally represented as four dotted decimal octets
10000000110111111001110100010011
128 . 223 . 157 . 19
2726252423222120
00010011

## Slide 8: Prefixes
Transforming Learning, Research and Working Environments using ICT
•
•
32 bits
27 bits 5 bits
A range of IP addresses is given as a prefix, e.g. 192.0.2.128/27 In this example:
How many addresses are available?
What are the lowest and highest addresses?
Prefix /27
Host

## Slide 9: Prefixes
Transforming Learning, Research and Working Environments using ICT
•
•
32 bits
27 bits 5 bits
A range of IP addresses is given as a prefix, e.g. 192.0.2.128/27 In this example:
How many addresses are available?
  Number of bits for the host = 32 – 27 = 5 bits
  Number of available addresses = 25 = 32
Prefix /27
Host

## Slide 10: Prefix Calculation
Transforming Learning, Research and Working Environments using ICT
192 . 0 . 2 . 128
11000000000000000000001010000000
Prefix length /27 → First 27 bits are fixed

## Slide 11: Prefix Calculation
Transforming Learning, Research and Working Environments using ICT
192 . 0 . 2 . 128
11000000000000000000001010000000
Prefix length /27 → First 27 bits are fixed
Lowest address:
11000000000000000000001010000000
192 . 0 . 2 . 128

## Slide 12: Prefix Calculation
Transforming Learning, Research and Working Environments using ICT
192 . 0 . 2 . 128
11000000000000000000001010000000
Prefix length /27 → First 27 bits are fixed
Lowest address:
11000000000000000000001010000000
192 . 0 . 2 . 128
Highest address:
11000000000000000000001010011111
192 . 0 . 2 . 159

## Slide 13: IPv4 “Golden Rules”
Transforming Learning, Research and Working Environments using ICT
32 bits
27 bits 5 bits
All hosts on the same L2 network must share the same prefix
All hosts with the same prefix have different host part
Host part of all-zeros and all-ones are reserved
Prefix /27
Host

## Slide 14: Golden Rules for 192.0.2.128/27
Transforming Learning, Research and Working Environments using ICT
•
•
•
•
Lowest 192.0.2.128 = network address Highest 192.0.2.159 = broadcast address Usable: 192.0.2.129 to 192.0.2.158
Number of usable addresses: 32 - 2 = 30

## Slide 15: Exercises
Transforming Learning, Research and Working Environments using ICT
•
Network 10.10.10.0/25
How many addresses in total?
How many usable addresses?
What are the lowest and highest usable addresses?

## Slide 16: Exercises
Transforming Learning, Research and Working Environments using ICT
•
Prefix length /25 → First 25 bits are fixed
Network 10.10.10.0/25
How many addresses in total?
How many usable addresses?
What are the lowest and highest usable addresses?
Hint…
10 . 10 . 10 . 0
00001010000010100000101000000000
00001010000010100000101001111111

## Slide 17: Exercises
Transforming Learning, Research and Working Environments using ICT
•
Network 10.10.10.0/25
How many addresses in total?
  Number of host bits is 32 – 25 = 7
  Number of addresses is 27 = 128
How many usable addresses?
  Network and broadcast addresses are unusable (2 ip addresses)
  Number of usable address is 128 – 2 = 126
What are the lowest and highest usable addresses?
  First IP address (network address) is 10.10.10.0 and last IP address (broadcast address) is 10.10.10.127. Both of them are unusable.
  First usable IP address is 10.10.10.1 and last usable address is 10.10.10.126

## Slide 18: An Edge Case
Transforming Learning, Research and Working Environments using ICT
How many usable addresses in a /30 prefix?
What is this used for?
– (Note: modern routers support /31 for this purpose to reduce IPv4 address wastage)

## Slide 19: An Edge Case
Transforming Learning, Research and Working Environments using ICT
How many usable addresses in a /30 prefix?
Number of host bits is 32 – 30 = 2
Number of addresses is 22 = 4
Number of usable address is 4 – 2 = 2
What is this used for?
Used for Point-to-Point links

## Slide 20: Netmask
Transforming Learning, Research and Working Environments using ICT
•
•
•
Netmask is just an alternative (old) way of writing the prefix length A ‘1’ for a prefix bit and ‘0’ for a host bit
Hence N x 1’s followed by (32-N) x 0’s
/27 =
11111111111111111111111111100000
255 . 255 . 255 . 224
How did we get to 224?

## Slide 21: Netmask
Transforming Learning, Research and Working Environments using ICT
/27 =
11111111111111111111111111100000
255 . 255 . 255 . 224
How did we get 224?
1. 256 – 2 (32-27)
2. 256 – 25
3. 256 – 32 = 224
What about a “/26” ? What about a “/28” ?
https://nsrc.org/workshops/2009/summer/ref/netmask- table.html

## Slide 22: Subnetting
Transforming Learning, Research and Working Environments using ICT
•
Since each L2 network needs its own prefix, then if you route more than one network you need to divide your allocation
Ensure each prefix has enough IPs for the number of hosts on that network
•
End User Allocation
Subnets

## Slide 23: Subnetting Example
Transforming Learning, Research and Working Environments using ICT
You have been given 192.0.2.128/27
However, you want to build two Layer 2 networks and route between them
The Golden Rules demand a different prefix for each network Let’s split this address space into two equal-sized pieces

## Slide 24: Subnetting /27
Transforming Learning, Research and Working Environments using ICT
192 . 0 . 2 . 128
11000000000000000000001010000000
Move one bit from host part to prefix

## Slide 25: Subnetting /27
Transforming Learning, Research and Working Environments using ICT
192 . 0 . 2 . 128
11000000000000000000001010000000
Move one bit from host part to prefix
We now have two /28 prefixes
11000000000000000000001010000000
192 . 0 . 2 . 128

## Slide 26: Subnetting /27
Transforming Learning, Research and Working Environments using ICT
192 . 0 . 2 . 128
11000000000000000000001010000000
Move one bit from host part to prefix
We now have two /28 prefixes
11000000000000000000001010000000
192 . 0 . 2 . 128
Second prefix:
11000000000000000000001010010000
192 . 0 . 2 . 144
How did we get “144” for the second prefix?

## Slide 27: Check correctness
Transforming Learning, Research and Working Environments using ICT
Expand each new prefix into lowest and highest
Ranges should not overlap
– 192.0.2.128/28
Lowest (network) = 192.0.2.128
Highest (broadcast) = 192.0.2.143
– 192.0.2.144/28
Lowest (network) = 192.0.2.144
Highest (broadcast) = 192.0.2.159
– How many usable addresses now?

## Slide 28: Aggregation tree
Transforming Learning, Research and Working Environments using ICT
•
•
Continue to divide prefixes as required Can visualise this as a tree
/24
/25
/25
/26
/26
/27
/27
/27
/27

## Slide 29
Transforming Learning, Research and Working Environments using ICT
Questions about IPv4?

## Slide 30: IPv6 addresses
Transforming Learning, Research and Working Environments using ICT
128-bit binary number
– How many unique addresses in total?

## Slide 31: IPv6 addresses
Transforming Learning, Research and Working Environments using ICT
•
128-bit binary number
How many unique addresses in total?
3.402823669209 x1038
Conventionally represented in hexadecimal – 8 words of 16 bits, separated by colons
2607:8400:2880:0004:0000:0000:80DF:9D
13
•

## Slide 32: IPv6 addresses
Transforming Learning, Research and Working Environments using ICT
•
128-bit binary number
How many unique addresses in total?
3.402823669209 x1038
Conventionally represented in hexadecimal – 8 words of 16 bits, separated by colons
2607:8400:2880:0004:0000:0000:80DF:9D
Leading zer1o3s can be dropped
The largest contiguous run of all-zero words can be replaced by "::” (see RFC5952)
2607:8400:2880:0004:0000:0000:80DF:9D
216307:8400:2880:4::80DF:9D13
•
•
•

## Slide 33: Hexadecimal
Transforming Learning, Research and Working Environments using ICT
0000 | 0 | 1000 | 8
0001 | 1 | 1001 | 9
0010 | 2 | 1010 | A
0011 | 3 | 1011 | B
0100 | 4 | 1100 | C
0101 | 5 | 1101 | D
0110 | 6 | 1110 | E
0111 | 7 | 1111 | F
0000 | = | 0000000000000000
FFFF | = | 1111111111111111

## Slide 34: IPv6 rules
Transforming Learning, Research and Working Environments using ICT
•
•
With IPv6, every subnet is /64 (*1)
The remaining 64 bits can be assigned by hand, or picked automatically
all-zeros address is reserved (*1) - Subnet-Router Anycast address
There are special prefixes
e.g. link-local addresses start with FE80::
Total available IPv6 space is ≈ 261 subnets
•
•
(*1) Except /127 recommended for point-to-point links (RFC 6164), in which case the all-zeros address is allowed

## Slide 35: IPv6 addressing
Transforming Learning, Research and Working Environments using ICT
•
Typical end-user allocation is /48
•
How many /64 networks can you build from a /48 allocation?
/48
assigned address space
network ID
network prefix
/64
host ID
/64

## Slide 36: IPv6 addressing
Transforming Learning, Research and Working Environments using ICT
•
Typical end-user allocation is /48
•
How many /64 networks can you build from a /48 allocation?
IPv6 address is 128 bits which means you have 128 – 64 – 48 = 16 bits
Number of networks = 216 = 65,536
/48
assigned address space
network prefix
/64
network ID
host ID
/64

## Slide 37: IPv6 addressing
Transforming Learning, Research and Working Environments using ICT
You are assigned 2001:DB8:123::/48
– 2001:0DB8:0123:0000:0000:0000:0000:0000
Lowest /64 network?

## Slide 38: IPv6 addressing
Transforming Learning, Research and Working Environments using ICT
•
You are assigned 2001:DB8:123::/48
– 2001:0DB8:0123:0000:0000:0000:0000:0000
Lowest /64 network?
– 2001:DB8:123:0000::/64
– written simply 2001:DB8:123::/64
•

## Slide 39: IPv6 addressing
Transforming Learning, Research and Working Environments using ICT
You are assigned 2001:DB8:123::/48
– 2001:0DB8:0123:0000:0000:0000:0000:0000
Lowest /64 network?
– 2001:DB8:123:0000::/64
written simply 2001:DB8:123::/64
Highest /64 network?
2001:DB8:123:FFFF::/64

## Slide 40: Ways to allocate the host part
Transforming Learning, Research and Working Environments using ICT
Do it automatically from MAC address – “stateless autoconfiguration”
– Not recommended for servers: if you change the NIC then the IPv6 address changes!

## Slide 41: Ways to allocate the host part
Transforming Learning, Research and Working Environments using ICT
Do it automatically from MAC address – “stateless autoconfiguration”
– Not recommended for servers: if you change the NIC then the IPv6 address changes!
Can number sequentially from 1, or use the last octet of the IPv4 address

## Slide 42: Ways to allocate the host part
Transforming Learning, Research and Working Environments using ICT
Do it automatically from MAC address – “stateless autoconfiguration”
Not recommended for servers: if you change the NIC then the IPv6 address changes!
Can number sequentially from 1, or use the last octet of the IPv4 address
Or embed the whole IPv4 address
e.g. 2607:8400:2880:4::80DF:9D13
80DF9D13 hex = 128.223.157.19 in decimal
Can write 2607:8400:2880:4::128.223.157.19

## Slide 43: Notes on IPv6
Transforming Learning, Research and Working Environments using ICT
•
•
•
Broadly similar to IPv4 “ARP” is replaced by “NDP”
IPv6 client configuration options
Stateless autoconf (router advertisements)
Stateless autoconf + stateless DHCPv6
Stateful DHCPv6
Interfaces typically get both a link-local address and one or more routable prefixes
“Dual stack” = v4 and v6 side-by-side
•

## Slide 44
Transforming Learning, Research and Working Environments using ICT
Questions about IPv6?

## Slide 45
Transforming Learning, Research and Working Environments using ICT
Hierarchical address allocation
IPv4 / IPv6
IANA

## Slide 46: Hierarchical address allocation
Transforming Learning, Research and Working Environments using ICT
IPv4 / IPv6
IANA
RIR

## Slide 47: Hierarchical address allocation
Transforming Learning, Research and Working Environments using ICT
IPv4 / IPv6
IANA
RIR
LIR/ISP

## Slide 48: Hierarchical address allocation
Transforming Learning, Research and Working Environments using ICT
IPv4 / IPv6
IANA
RIR
LIR/ISP
End User

## Slide 49: IPv4 Address Distribution
Transforming Learning, Research and Working Environments using ICT
•
IPv4 addresses
Distributed by RIRs according to demonstrated need
Have almost all run out
RIRs have IPv4 run out policies
  E.g. one off assignment from a limited pool
Typical Campus:
Small public address block
  For public servers, NAT pools
  Anything from /28 to /21 depending on RIR region/upstream
Private address block
  For internal end users, network management, etc
•

## Slide 50: IPv6 Address Distribution
Transforming Learning, Research and Working Environments using ICT
•
IPv6 addresses
Network operators receive minimum of /32
  Includes RENs, University Campuses, etc
End-sites receive /48
Smallest subnet size is /64
Typical Single Campus:
/48 divided out amongst buildings
Typical Multi-Campus or Multi-Faculty:
/32 divided out amongst Campuses
  /48 per campus
•
•

## Slide 51
Transforming Learning, Research and Working Environments using ICT
Questions about IP Address Distribution?

## Slide 52: Designing an Address Plan
Transforming Learning, Research and Working Environments using ICT
•
Now we will look at how to design an address plan for a simple campus
– Let’s use our campus from the fibre pricing exercise
Border Router
Central Servers for campus
Fiber optic links to remote buildings
300m
500m 800m 200m
Copper cable
1000m
Core Router
500m

## Slide 53: Designing an Address Plan
Transforming Learning, Research and Working Environments using ICT
•
The following table shows the host allocation for each part of that campus
Network | Number of Devices
Border Router to Core Router | 2
Server Network | 23
Science Building | 120
Arts Building | 52
Engineering Building | 200
Library | 80
Administration Building | 40
Languages Building | 30
Staff & Student Hostel | 60
Wireless Network | 350

## Slide 54: Designing an Address Plan
Transforming Learning, Research and Working Environments using ICT
The University has the following address space:
– 172.16.0.0/16
– 2001:DB8:8::/48
IPv4 Address block IPv6 Address block
•
We will now use these address blocks to design an IPv4 and IPv6 address plan for the campus

## Slide 55: IPv4 Plan
Transforming Learning, Research and Working Environments using ICT
•
Using the previous table, let’s add a column to show the subnet sizes for each function
Network | Number of Devices | IPv4 Subnet Size
Border Router to Core Router | 2 | /30
Server Network | 23 | /27
Science Building | 120 | /25
Arts Building | 52 | /26
Engineering Building | 200 | /24
Library | 80 | /25
Administration Building | 40 | /26
Languages Building | 30 | /26
Staff & Student Hostel | 60 | /25
Wireless Network | 350 | /23

## Slide 56: IPv4 Plan
Transforming Learning, Research and Working Environments using ICT
•
And now let’s assign address blocks accordingly
Network | Number of Devices | IPv4 Subnet Size | Allocation
Border Router to Core Router | 2 | /30 | 172.16.0.0/30
Server Network | 23 | /27 | 172.16.0.32/27
Science Building | 120 | /25 | 172.16.5.0/25
Arts Building | 52 | /26 | 172.16.5.128/26
Engineering Building | 200 | /24 | 172.16.1.0/24
Library | 80 | /25 | 172.16.4.0/25
Administration Building | 40 | /26 | 172.16.0.192/26
Languages Building | 30 | /26 | 172.16.5.192/26
Staff & Student Hostel | 60 | /25 | 172.16.4.128/25
Wireless Network | 350 | /23 | 172.16.2.0/23

## Slide 57: IPv4 Plan Explanation
Transforming Learning, Research and Working Environments using ICT
Keep 172.16.0.0/24 for infrastructure and administrative network
–
–
Border Router to Core Router gets 172.16.0.0/30
Server Network gets 172.16.0.32/27 which is the first available /27 prefix in that range after the Border Router to Core Router assignment but any free /27 prefix in 172.16.0.0/24 range can be used
– Administration building gets 172.16.0.192/26
•
Assign the biggest subnet first
–
–
Wireless gets 172.16.2.0/23 (172.16.2.0→172.16.3.255)
Remember that a /23 prefix is equivalent two /24 prefixes, so the first available /23 prefix is 172.16.2.0/23. You can use any free /23 prefixes in the 172.16.0.0/16 pool.
Then we assign the /24 which is the next biggest subnet
– 172.16.1.0/24 goes to Engineering

## Slide 58: IPv4 Plan Explanation
Transforming Learning, Research and Working Environments using ICT
Then we assign the /25s
–
–
–
172.16.4.0/25 goes to the Library
172.16.4.128/25 goes to the Staff and Student Hostel 172.16.5.0/25 goes to the Science building
Finally we assign the /26s
–
–
Arts Building gets 172.16.5.128/26
Languages Building gets 172.16.5.192/26.
It is easier to do the big pieces first, and then fill in the gaps with the smaller subnets
Use of the aggregation tree concept covered in the previous section is very helpful in the creation of an IPv4 plan

## Slide 59: IPv4 Plan Conclusion
Transforming Learning, Research and Working Environments using ICT
•
We have addressed our network using 172.16.0.0 through to 172.16.5.255
This is contained within the 172.16.0.0/21 address block An example of an efficient use of IPv4 address space
•
•

## Slide 60: IPv6 Plan
Transforming Learning, Research and Working Environments using ICT
Let’s repeat now for IPv6
– Only subnet size is /64 – so this is easy!
Network | Number of Devices | IPv6 Subnet Size
Border Router to Core Router | 2 | /127
Server Network | 23 | /64
Science Building | 120 | /64
Arts Building | 52 | /64
Engineering Building | 200 | /64
Library | 80 | /64
Administration Building | 40 | /64
Languages Building | 30 | /64
Staff & Student Hostel | 60 | /64
Wireless Network | 350 | /64

## Slide 61: IPv6 Addressing Notes
Transforming Learning, Research and Working Environments using ICT
•
Campus gets a whole /48
So let’s not think like IPv4 when we design our plan
We have 2001:DB8:8:XXYY::/48 available to us
  XX can be used to count functions – this gives us a total of 256 /56s in campus
  YY can be used to count subnets within the function – this gives us a total of 256
/64s in each function
  Each function might be a Faculty, or a Building, or Core Infrastructure

## Slide 62: IPv6 Addressing Notes
Transforming Learning, Research and Working Environments using ICT
Let’s do this:
One /56 for Campus Network Infrastructure
  This gives us 256 possible /64s for Campus Network Infrastructure
  We will use one /64 for the point to point link
  We will use another /64 for the servers
One /56 for each Building
  This gives us 256 possible /64s within each Building
  But we only have one LAN per Building in this example
– We have plenty of room to add more in the future

## Slide 63: IPv6 Plan
Transforming Learning, Research and Working Environments using ICT
And now let’s assign address blocks accordingly
Network | Number of Devices | IPv6 Subnet Size | Allocation
Border Router to Core Router | 2 | /127 | 2001:DB8:8:0000::/64
Server Network | 23 | /64 | 2001:DB8:8:0010::/64
Science Building | 120 | /64 | 2001:DB8:8:0100::/64
Arts Building | 52 | /64 | 2001:DB8:8:0200::/64
Engineering Building | 200 | /64 | 2001:DB8:8:0300::/64
Library | 80 | /64 | 2001:DB8:8:0400::/64
Administration Building | 40 | /64 | 2001:DB8:8:0500::/64
Languages Building | 30 | /64 | 2001:DB8:8:0600::/64
Staff & Student Hostel | 60 | /64 | 2001:DB8:8:0700::/64
Wireless Network | 350 | /64 | 2001:DB8:8:0800::/64

## Slide 64: Further IPv6 Address Plan Advice
Transforming Learning, Research and Working Environments using ICT
Use the “nibbles” in the IPv6 address to indicate function
– Nibble is 4 bits – each character in the IPv6 address represents 4 bits.
You might do this for 2001:DB8:8:XYZZ::/48
Use X=0 for the campus backbone infrastructure
There are many variations on this theme
But use the “nibbles” to indicate function as it makes the address plan easy, memorable, and scalable
X | The Faculty | 15 Faculties
Y | The Department | 16 Departments per Faculty
ZZ | The LANs | 256 per Department

## Slide 65
Transforming Learning, Research and Working Environments using ICT
Questions?

## Slide 66
Transforming Learning, Research and Working Environments using ICT
Transforming Learning, Research and Working Environments using ICT
“This work was developed with resources and expertise provided by the Network Startup Resource Center (NSRC) and the University of Oregon.”

## Slide 67
www.kenet.or.ke
Jomo Kenyatta Memorial
Library, University of Nairobi
P. O Box 30244-00100, Nairobi.
0732 150 500 / 0703 044 500
Thank You