## Slide 1
Track 2: Module 1: Introduction to IP Addressing and Routing
Transforming Learning, Research and Working Environments using ICT

## Slide 2: Fundamentals of IP Addressing
Transforming Learning, Research and Working Environments using ICT
Define IP addressing fundamentals, including the structure and types of IPv4 and IPv6 addresses.
Differentiate between IPv4 and IPv6, and explain the role of IP addressing in network security.
Apply subnetting techniques using Subnet Masks and CIDR to enable network segmentation.
Understand the principles of Network Address Translation (NAT) and network IP address planning.
Explain the fundamentals of routing and identify common routing vulnerabilities.
Identify and apply IP-based security controls, including ACLs, Firewall Rules, and VPNs.

## Slide 3: Fundamentals of IP Addressing
Transforming Learning, Research and Working Environments using ICT

## Slide 4: Introduction to IP Addresses
Image Source: Huawei Technologies Co., LTD
What are they?
Why are they important?
Notes: What they are: Unique numerical labels assigned to every device on a network (e.g., computers, servers, printers). Think of it as a device’s street address on the internet.
Why they're important: IP addresses enable devices to communicate with each other. They are crucial for addressing and routing data packets to their correct destination. Without them, there is no network communication.

## Slide 5: IPv4 Header
Image Source: Huawei Technologies Co., LTD
Notes: What they are: Unique numerical labels assigned to every device on a network (e.g., computers, servers, printers). Think of it as a device’s street address on the internet.
Why they're important: IP addresses enable devices to communicate with each other. They are crucial for addressing and routing data packets to their correct destination. Without them, there is no network communication.

## Slide 6: The Role of IP Addressing in Network Security
Transforming Learning, Research and Working Environments using ICT
A Primary Identifier
Logging and forensics
Access Control Lists (ACLs)
Notes: A foundation of security: IP addresses are the primary identifiers used in security tools. A firewall, for example, makes decisions to permit or deny traffic based on source and destination IP addresses.
Logging and forensics: When a security incident occurs, network logs often contain IP addresses of the involved devices, which is critical for tracing the attack path and identifying compromised systems.
Access Control Lists (ACLs): These are lists of rules that control network traffic, and they are almost always based on IP addresses.

## Slide 7: IPv4 vs. IPv6
Transforming Learning, Research and Working Environments using ICT
IPv4: The current standard, using 32-bit addresses (e.g., 192.168.1.1).
IPv6: The next-generation protocol, using 128-bit addresses (e.g., 2001:0db8:85a3:0000:0000:8a2e:0370:7334).
Key Differences: The most significant difference is the address space. IPv4 is running out of addresses, while IPv6 provides a virtually unlimited supply. IPv6 also has a simpler header format and built-in security features like IPSec.

## Slide 8: IPv4 Address Format
Image Source: https://www.cloudns.net/blog/what-is-ipv4-everything-you-need-to-know/
Notes: IPv4 is short for Internet Protocol version 4. The 4th version of the Internet protocol (IP) is still a popular protocol for communication over the Internet. It establishes the rules and limitations for communication over the Internet or on a local network. Thanks to the IP, we can have interconnected network routing with packet forwarding because it defines the format, and the communications, use IPv4 addresses, and routes data.
In contrast to the transmission Control Protocol (TCP), the Ipv4 protocol does not need to guarantee delivery, and that makes it a connectionless protocol. It functions on the best-effort delivery model and makes it fast.
IPv4 was first described in 1981 by the Internet Engineering Task Force (IETF, RFC 791) and was later adopted by the Department of Defense of The USA in 1982, SATNET in 1982, and ARPANET in 1983.
We can’t miss talking about IPv4 addresses too. An IPv4 address is a 32-bit address that identifies a device on a network. It is made of 4 groups of numbers (octets) with up to 3 numbers each. The IPv4 will identify the network and the individual host on the network.
The problems that IPv4 has are the following:
IP address exhaustion. The business needs for IP addresses can’t be satisfied with IPv4 addresses only, so they are already migrating to IPv6.
No IPsec support by default. You can still enable it, but it is a lot easier with the newer IP.
Limited header in which you can’t add extra parameters.
It is getting too expensive with prices above $25 per IP address.

## Slide 9: IPv4 Classes
Transforming Learning, Research and Working Environments using ICT
Notes: Source: https://www.adroitacademy.com/blog/What-are-the-classes-of-IPv4-Addresses IP address classification refers to the categorization of IP addresses into different classes based on their network structure and address range. This classification was relevant mainly in the context of IPv4 (Internet Protocol version 4), as it used a fixed-length 32-bit address space. With the introduction of IPv6 (Internet Protocol version 6), which has a much larger address space, the concept of IP address classification became less significant.
In IPv4, the IP address is divided into two parts: the network part and the host part. The division between the network and host parts is determined by the subnet mask. The subnet mask is a 32-bit value that consists of consecutive 1 (binary) in the network part followed by consecutive 0 (binary) in the host part.
There are five IPv4 address classes (Class A to Class E) designated as follows:
Class A (1.0.0.0 to 126.255.255.255):
Class A addresses have the first bit of the IP address set to 0 (MSB), and the network part occupies the first octet (8 bits). The remaining three octets (24 bits) represent the host part. Class A addresses were originally intended for large networks and have a vast number of host addresses.
Class B (128.0.0.0 to 191.255.255.255):
Class B addresses have the first two bits of the IP address set to 10 (MSB), and the network part occupies the first two octets (16 bits). The remaining two octets (16 bits) represent the host part. Class B addresses were designed for medium-sized networks.
Class C (192.0.0.0 to 223.255.255.255):
Class C addresses have the first three bits of the IP address set to 110 (MSB), and the network part occupies the first three octets (24 bits). The remaining octet (8 bits) represents the host part. Class C addresses were intended for small networks.
Class D (224.0.0.0 to 239.255.255.255):
Class D addresses have the first four bits of the IP address set to 1110 (MSB). These addresses are used for multicast purposes, where data can be sent to multiple hosts at a time.
Class E (240.0.0.0 to 255.255.255.255):
Class E addresses have the first four bits of the IP address set to 1111 (MSB). Class E addresses were reserved for experimental purposes and were not meant for general use.
It's important to note that IP address classification based on classes is mostly a historical concept. In modern networking, subnetting and Classless Inter-Domain Routing (CIDR) are commonly used techniques to allocate IP addresses more efficiently and flexibly, regardless of the traditional class boundaries. CIDR allows for the allocation of IP addresses in variable-sized blocks, which enables better address utilization and more efficient routing of the network traffic.

## Slide 10: IPv4 Address Types
Transforming Learning, Research and Working Environments using ICT
Network address: identifies a network.
Broadcast address: a special address used to send data to all hosts on the network.
Available addresses: IP addresses that can be allocated to device interfaces on the network.

## Slide 11: Special IP Address
Source: https://www.avast.com/c-ip-address-public-vs-private
Limited broadcast address – 255.255.255.255
Any IP Address – 0.0.0.0
Loopback Address – 127.0.0.0/8
Link-Local Address – 169.254.0.0/24
Notes: Limited - It can be used as a destination address and traffic destined for it is sent to all hosts on the network segment to which the address belongs. (Its usage is restricted by a gateway).
Any - It is an address of any network.
Addresses in this block refer to source hosts on "this" network.
Loopback - It is used to test the software system of a test device.
Link-Local - If a host fails to automatically obtain an IP address, the host can use an IP address in this address block for temporary communication.

## Slide 12: Public vs. Private IP Addresses
Source: https://www.avast.com/c-ip-address-public-vs-private
Notes: Public IP Addresses
Globally Unique: Every public IP address on the internet is unique, allowing data to be routed to the correct network.
Routable: These addresses are accessible from anywhere on the internet.
Assigned by ISP: Your Internet Service Provider (ISP) assigns a public IP address to your router.
For Internet Communication: They are used to send and receive information over the internet.
Private IP Addresses
Locally Unique: These addresses are only unique within a private network. They can be reused in different private networks without conflict.
Not Routable: They are not accessible from the public internet; they are only used for communication between devices within the same local network.
Assigned by Router: Your router assigns private IP addresses to all the devices connected to your network (e.g., your phone, laptop, smart TV).
For Local Communication: They are used for devices to communicate with each other within your home or office network.

## Slide 13: Network Address Translation
Image Source: https://en.wikipedia.org/wiki/Network_address_translation
Discussion
  What is NAT?
  Why is NAT important?
Notes: Network address translation (NAT) is a method of mapping an IP address space into another by modifying network address information in the IP header of packets while they are in transit across a traffic routing device.[1] The technique was initially used to bypass the need to assign a new address to every host when a network was moved, or when the upstream Internet service provider was replaced but could not route the network's address space. It is a popular and essential tool in conserving global address space in the face of IPv4 address exhaustion. One Internet-routable IP address of a NAT gateway can be used for an entire private network.[2]
As network address translation modifies the IP address information in packets, NAT implementations may vary in their specific behavior in various addressing cases and their effect on network traffic. Vendors of equipment containing NAT implementations do not commonly document the specifics of NAT behavior.

## Slide 14: Subnetting, and Network Segmentation
Transforming Learning, Research and Working Environments using ICT

## Slide 15: Subnet Masks and CIDR
Transforming Learning, Research and Working Environments using ICT
Subnet mask: A 32-bit number that separates the network portion of an IP address from the host portion.
CIDR (Classless Inter-Domain Routing): A more flexible way to define a subnet mask, using a / followed by the number of bits in the network portion (e.g., 192.168.1.0/24). This is the modern, efficient method for IP allocation.
Notes: Why is subnetting important?
A network number is divided into multiple subnets, and each subnet is allocated to a separate broadcast domain.
In this way, the broadcast domain is smaller, and the network planning is more reasonable.
IP addresses are properly used.
If broadcast domain is too large, broadcasts are going to overwhelm the network

## Slide 16: The Security Power of Subnetting
Transforming Learning, Research and Working Environments using ICT
Network Segmentation: Subnetting allows you to divide a single large network into smaller, isolated logical segments. This is a core cybersecurity strategy.
Containment: If an attacker breaches one subnet (e.g., the student network), they are contained within that segment and cannot easily move to a more critical segment (e.g., the financial aid server farm) without first bypassing a firewall or router.

## Slide 17: Computing Subnets
Transforming Learning, Research and Working Environments using ICT
An existing class C network segment is 192.168.1.0/24. Use the VLSM to allocate IP addresses to three subnets.

## Slide 18: Network IP Address Planning
Image Source: Huawei Technologies Co., LTD
IP address planning objectives are to achieve easy management, easy scalability, and high utilization.
Notes: Planning rules:
  Uniqueness: Each host on an IP network must have a unique IP address.
  Continuity: Contiguous addresses can be summarized easily in the hierarchical networking. Route summarization reduces the size of the routing table and speeds up route calculation and route convergence.
  Scalability: Addresses need to be properly reserved at each layer, ensuring the contiguous address space for route summarization when the network is expanded. Re-planning of addresses and routes induced by network expansion is therefore prevented.
  Combination of topology and services: Address planning is combined with the network topology and network transport service to facilitate route planning and quality of service (QoS) deployment. Appropriate IP address planning helps you easily determine the positions of devices and types of services once you read the IP addresses.

## Slide 19: Introduction to Routing and Routing Security
Transforming Learning, Research and Working Environments using ICT

## Slide 20: What is a Router?
Image Source: Huawei Technologies Co., LTD
The Network Traffic Cop: A router's primary job is to connect different networks and forward data packets between them.
How it works: It inspects the destination IP address of a packet and consults its routing table to determine the best path to send it.
Notes: Planning rules:
  Uniqueness: Each host on an IP network must have a unique IP address.
  Continuity: Contiguous addresses can be summarized easily in the hierarchical networking. Route summarization reduces the size of the routing table and speeds up route calculation and route convergence.
  Scalability: Addresses need to be properly reserved at each layer, ensuring the contiguous address space for route summarization when the network is expanded. Re-planning of addresses and routes induced by network expansion is therefore prevented.
  Combination of topology and services: Address planning is combined with the network topology and network transport service to facilitate route planning and quality of service (QoS) deployment. Appropriate IP address planning helps you easily determine the positions of devices and types of services once you read the IP addresses.

## Slide 21: IP Routing Table
Image Source: Huawei Technologies Co., LTD
Notes: Routes are the path information used to guide packet forwarding.
A routing device is a network device that forwards packets to a destination subnet based on routes. The most common routing device is a router.
A routing device maintains an IP routing table that stores routing information.
A route contains the following information:
  Destination: identifies a destination subnet.
  Mask: identifies a subnet together with a destination IP address.
  Outbound interface: indicates the interface through which a data packet is sent out of the local router.
  Next hop: indicates the next-hop address used by the router to forward the data packet to the destination subnet.
  The information identifies the destination subnet and specifies the path for forwarding data packets.
Routers discover routes using multiple methods.
A router selects the optimal route and installs it in its IP routing table.
The router forwards IP packets based on routes in the IP routing table.
Routers manage path information by managing their IP routing tables.

## Slide 22: Types of Routes
Image Source: Huawei Technologies Co., LTD
Notes: Static Routing: Network administrator manually configures routes. Simple, secure, but not scalable for large networks.
Dynamic Routing: Routers use protocols (like OSPF or BGP) to automatically share routing information and find the best paths. Highly scalable but introduces new security vulnerabilities.

## Slide 23: Routing Vulnerabilities
Transforming Learning, Research and Working Environments using ICT
BGP Hijacking: An attacker can maliciously broadcast false routing information, tricking the internet into sending traffic intended for a legitimate network to the attacker's network instead. This is a severe threat.
Case Study (2008 Pakistan Telecom incident): A well-known example where a Pakistani ISP tried to block YouTube within its country by announcing a route to the video service. They accidentally leaked this announcement to the wider internet, causing YouTube to be inaccessible globally for over an hour. This illustrates how a misconfigured or malicious routing announcement can have a massive impact.
Notes: Static Routing: Network administrator manually configures routes. Simple, secure, but not scalable for large networks.
Dynamic Routing: Routers use protocols (like OSPF or BGP) to automatically share routing information and find the best paths. Highly scalable but introduces new security vulnerabilities.

## Slide 24: IPv6 Security: Deployment and Protection
Transforming Learning, Research and Working Environments using ICT

## Slide 25: IPv6 Address
Image Source: http://ipcisco.com/lesson/ipv6-address/
Notes: Break down the 128-bit address into its components: Global Routing Prefix, Subnet ID, and Interface ID. Explain how this structure is designed for a hierarchical and scalable internet.

## Slide 26: IPv6 Address Header
Image Source: Huawei Technologies Co., LTD

## Slide 27: IPv6 Address Classification
Image Source: Huawei Technologies Co., LTD
Notes: Unicast address: identifies an interface. A packet destined for a unicast address is sent to the interface having that unicast address. In IPv6, an interface may have multiple IPv6 addresses. In addition to GUAs, ULAs, and LLAs, IPv6 has the following special unicast addresses:
  Unspecified address: 0:0:0:0:0:0:0:0/128, or ::/128. The address is used as the source address of some packets, for example, Neighbor Solicitation (NS) messages sent during DAD or request packets sent by a client during DHCPv6 initialization.
  Loopback address: 0:0:0:0:0:0:0:1/128, or ::1/128, which is used for local loopback (same function as 127.0.0.1 in IPv4). The data packets sent to ::/1 are actually sent to the local end and can be used for loopback tests of local protocol stacks.
Multicast address: identifies multiple interfaces. A packet destined for a multicast address is sent to all the interfaces joining in the corresponding multicast group. Only the interfaces that join a multicast group listen to the packets destined for the corresponding multicast address.
Anycast address: identifies a group of network interfaces (usually on different nodes). A packet sent to an anycast address is routed to the nearest interface having that address, according to the router's routing table.
IPv6 does not define any broadcast address. On an IPv6 network, all broadcast application scenarios are served by IPv6 multicast.

## Slide 28: IPv6 Security Challenges
Transforming Learning, Research and Working Environments using ICT
NDP Attacks: Neighbor Discovery Protocol (NDP) is the IPv6 equivalent of ARP. It is vulnerable to attacks like neighbor spoofing, which can be used to redirect traffic.
Large Address Space: The vastness of IPv6 addresses can be a challenge for scanning and monitoring, but it also makes brute-force attacks difficult.

## Slide 29: Transition Mechanisms and their Security Risks
Transforming Learning, Research and Working Environments using ICT
Dual-Stacking: Running both IPv4 and IPv6 on a device. The primary risk is misconfiguration, where an IPv6 service might be left insecurely exposed.
Tunneling: Encapsulating IPv6 packets inside IPv4 packets to traverse an IPv4 network. This can create "shadow networks" that are difficult to monitor and secure.

## Slide 30: IP Addressing, Routing, and DNS Security
Transforming Learning, Research and Working Environments using ICT

## Slide 31: How DNS Works with IP Addressing
Image Source:https://ipcisco.com/lesson/domain-name-system-overview/
The Phonebook of the Internet: DNS translates human-friendly domain names (e.g., university.ac.ke) into machine-readable IP addresses. IP addressing is the destination, DNS is how we find it.

## Slide 32: Threats to the DNS Service
Transforming Learning, Research and Working Environments using ICT
DNS Spoofing/Cache Poisoning: An attacker injects malicious data into a DNS resolver's cache, causing it to return an incorrect IP address for a domain. This redirects users to a fake website controlled by the attacker.
Case Study (2018 MyEtherWallet attack): A BGP hijacking attack was used to intercept traffic to Amazon's DNS service. This allowed the attackers to manipulate DNS queries for "myetherwallet.com," redirecting users to a phishing site and stealing their cryptocurrency. This demonstrates how routing and DNS vulnerabilities can be chained together for a successful attack.

## Slide 33: Mitigating DNS Threats
Transforming Learning, Research and Working Environments using ICT
DNSSEC (DNS Security Extensions): A suite of extensions that cryptographically signs DNS records to ensure their authenticity. This prevents DNS cache poisoning.
DNS Filtering: Using a secure DNS service that blocks access to known malicious domains.

## Slide 34: Putting It All Together: IP-Based Network Security Controls
Transforming Learning, Research and Working Environments using ICT

## Slide 35: Access Control Lists (ACLs)
Transforming Learning, Research and Working Environments using ICT
Function: ACLs are used on routers and firewalls to filter traffic based on rules. These rules are primarily based on source and destination IP addresses, but can also include ports and protocols.
Best Practice: The principle of least privilege—deny all traffic by default and only permit what is absolutely necessary.

## Slide 36: Firewall Rules
Transforming Learning, Research and Working Environments using ICT
Definition: A set of rules that governs a firewall's behavior. It is the core of network perimeter security.
Implementation: Demonstrate how to create a rule to block a specific IP address or an entire subnet from accessing a server.

## Slide 37: VPNs
Transforming Learning, Research and Working Environments using ICT
Purpose: To create a secure, encrypted tunnel between two endpoints (e.g., a remote user and the university network).
How it works: All data is encapsulated and encrypted, protecting it from eavesdropping, even if it traverses a public network.

## Slide 38: Network Logging and Monitoring
Transforming Learning, Research and Working Environments using ICT
The "Eyes" on the Network: Network devices should be configured to log IP-based events, such as failed connection attempts, traffic from suspicious IPs, and changes to routing tables.
Importance: These logs are essential for proactive threat detection and for incident response.

## Slide 39: Session Summary
Transforming Learning, Research and Working Environments using ICT
This session provided a comprehensive overview of IP addressing (IPv4 and IPv6), detailing address formats, types, and the principles of Network Address Translation (NAT). We covered practical skills like subnetting using CIDR for efficient network segmentation and security. Finally, we explored the fundamentals of routing and its security risks, and introduced core IP-based security controls such as ACLs, firewall rules, and VPNs to secure network environments.

## Slide 40
www.kenet.or.ke
Jomo Kenyatta Memorial
Library, University of Nairobi
P. O Box 30244-00100, Nairobi.
0732 150 500 / 0703 044 500
Thank You