## Slide 1
Ms. Anne Inapat
Sr. Systems Administrator
KENET
ainapat@kenet.or.ke
Transforming Learning, Research and Working Environments using ICT
Introduction to eduroam

## Slide 2: What is eduroam?
Transforming Learning, Research and Working Environments using ICT
eduroam (education roaming) is the secure, world-wide roaming access service developed for the international research and education community.
Purpose: eduroam allows students, researchers and staff from participating institutions to access Internet connectivity across campus and when visiting other participating institutions by simply opening their laptop.
Based On: WPA2 & IEEE 802.1X (network access control) – RADIUS (infrastructure to transport credentials) – Trust fabric (RADIUS hierarchy and policy)

## Slide 3: Global architecture overview
Transforming Learning, Research and Working Environments using ICT
The RADIUS hierarchy forwards user credentials securely to the users’ home institutions, where they are verified and validated.
To protect the privacy of the traffic from the user’s device to the wireless network, the latest up-to-date data encryption standards are used.
Notes: RADIUS Servers:
A linked hierarchy of RADIUS servers, including proxy servers, used to securely route authentication requests from a visiting institution to the user's home institution.
IEEE 802.1X Standard:
The underlying network access control standard used for authentication, which enables users to log in securely using their university-provided credentials.
Home Institution Credentials:
The usernames and passwords belonging to the user's home institution, which are kept secure and are forwarded for validation rather than being shared with the visited network.

## Slide 4: eduroam Architectural Components
Transforming Learning, Research and Working Environments using ICT
Database of Users i.e. LDAP, SQL,AD
Authentication server (Radius)
Access Point(authenticator)
Supplicant (module to authenticate)
Notes: RADIUS Servers:
A linked hierarchy of RADIUS servers, including proxy servers, used to securely route authentication requests from a visiting institution to the user's home institution.
IEEE 802.1X Standard:
The underlying network access control standard used for authentication, which enables users to log in securely using their university-provided credentials.
Home Institution Credentials:
The usernames and passwords belonging to the user's home institution, which are kept secure and are forwarded for validation rather than being shared with the visited network.

## Slide 5: AUTHENTICATION AND IEEE802.1x
Transforming Learning, Research and Working Environments using ICT
IEEE 802.1x encompasses the use of the Extensible Authentication Protocol (EAP)
  EAP is a container that carries the actual authentication data inside, the so-called EAP methods.
  EAP methods in use in eduroam are: PEAP, TTLS, TLS,FAST
  Until identity is proven:
    Allows only 802.1x Extensible Authentication Protocol (EAP) traffic to enter the network.
Notes: RADIUS Servers:
A linked hierarchy of RADIUS servers, including proxy servers, used to securely route authentication requests from a visiting institution to the user's home institution.
IEEE 802.1X Standard:
The underlying network access control standard used for authentication, which enables users to log in securely using their university-provided credentials.
Home Institution Credentials:
The usernames and passwords belonging to the user's home institution, which are kept secure and are forwarded for validation rather than being shared with the visited network.

## Slide 6: AUTHENTICATION AND IEE802.1x
Transforming Learning, Research and Working Environments using ICT
Notes: Supplicant: (Client) User device (e.g., laptop, phone) requesting authentication
Access Point: Provides WLAN access, forwards auth requests to local RADIUS server
Institutional RADIUS server: Authenticates own users or forwards to NRO
National RADIUS: Forwards requests within a country or to the global infrastructure
Top-Level RADIUS: Routes between countries or regions
RADIUS Proxy Chain: Forwards requests securely up/down the hierarchy

## Slide 7: How eduroam benefits institutions and end-users
Transforming Learning, Research and Working Environments using ICT
Secure Access: uses secure authentication protocols to verify users' identities, ensuring that only authorized individuals from participating institutions can connect to the network.
Enables Global Roaming: available at thousands of locations globally.
Federated Authentication: relies on a federated authentication system, meaning users authenticate using their credentials from their home institution.
Convenience: simplifies the process of accessing Wi-Fi for users who need to work or study at different institutions, no guest accounts.
Cost-Free: eduroam access is typically free for users from participating institutions.
Notes: https://www.pingidentity.com/en/resources/blog/post/radius-authentication.html#:~:text=Authentication%20Response:%20If%20the%20credentials%20match%2C%20the,don't%20match%2C%20an%20%E2%80%9CAccess%2DReject%E2%80%9D%20response%20is%20sent.

## Slide 8: Vendor hardware compatibility for eduroam
Transforming Learning, Research and Working Environments using ICT
Key Requirements:
Wi-fi router with WPA2/WPA3 wireless encryption support.
Support for the IEEE 802.1X protocol.
EAP Method Support: Device must support the EAP method chosen by your institution. Common EAP methods:
EAP-TTLS-PAP
PEAP
EAP-TLS
EAP-pwd In summary, if the device supports WPA2 + 802.1X and matches your institution's EAP method, it's ready for eduroam.
Notes: https://wiki.geant.org/pages/viewpage.action?pageId=121346284
https://confluence.terena.org/display/H2eduroam/Devices+that+are+compatible+with+eduroam

## Slide 9: Sources
Transforming Learning, Research and Working Environments using ICT
https://www.eduroam.org
https://en.wikipedia.org/wiki/IEEE_802.1X
https://wiki.geant.org
Notes: https://wiki.geant.org/pages/viewpage.action?pageId=121346284
https://confluence.terena.org/display/H2eduroam/Devices+that+are+compatible+with+eduroam

## Slide 10
www.kenet.or.ke
Jomo Kenyatta Memorial
Library, University of Nairobi
P. O Box 30244-00100, Nairobi.
0732 150 500 / 0703 044 500
Thank You