## Slide 1
Module 3: Setting up an Identity provider (IdP)
Transforming Learning, Research and Working Environments using ICT

## Slide 2
Transforming Learning, Research and Working Environments using ICT
Learning Objectives
By the end of this module, participants will be able to:
Deploy and configure FreeRADIUS as an IdP
Integrate FreeRADIUS with LDAP/Active Directory
Configure secure EAP authentication methods (PEAP, EAP-TTLS, EAP-TLS)
Set up and manage a Certificate Authority (CA) and client/server certificates
Perform authentication tests from CLI and mobile devices

## Slide 3
Transforming Learning, Research and Working Environments using ICT
Section 1: Installing and Configuring FreeRADIUS on Ubuntu
1.1 Prerequisites
Ubuntu Server 20.04 LTS (or higher)
Root/sudo access
Basic understanding of CLI

## Slide 4
Transforming Learning, Research and Working Environments using ICT
1.2 Installation Steps
sudo apt update
sudo apt install freeradius freeradius-ldap freeradius-utils

## Slide 5
Transforming Learning, Research and Working Environments using ICT
1.3 Configuration
Default config path: /etc/freeradius/
Key files:
  clients.conf: Define eduroam SPs and NAS clients
  users: Define local test users (temporary)
  mods-available/eap: EAP auth settings
  proxy.conf: Ream-based request forwarding

## Slide 6
Transforming Learning, Research and Working Environments using ICT
1.3 Configuration – Part 2
Note, radius is a complex service, while there is copious documentation some of it is only present in the config files themselves which require careful reading
One of the most important tools in understanding how config changes affect the radius server is this ability to run it by hand in debug mode.
Debug mode is enabled by running: freeradiusd –X
If you do that now you will note that it refuses to start

## Slide 7
Transforming Learning, Research and Working Environments using ICT
1.3 Configuration – Part 3
Key Config Files
  radiusd.conf: Master configuration file for the FreeRADIUS daemon
  Location: /etc/freeradius/radiusd.conf

## Slide 8
Transforming Learning, Research and Working Environments using ICT
1.3 Configuration – Part 3
Key Config Files
  clients.conf: Define clients (e.g. access points, wireless controllers) allowed to communicate with the RADIUS server
client 41.89.xx.xx { secret = secret-here nastype = other shortname = KTLR1 virtual_server = eduroam } client 192.168.0.0/16 { secret = testing123
nastype = other shortname = all-access-points virtual_server = eduroam }

## Slide 9
Transforming Learning, Research and Working Environments using ICT
Secret (Digression)
From RFC 2865:
The secret (password shared between the client and the RADIUS server) SHOULD be at least as large and unguessable as a well-chosen password. It is preferred that the secret be at least 16 octets. This is to ensure a sufficiently large range for the secret to provide protection against exhaustive search attacks. The secret MUST NOT be empty (length 0) since this would allow packets to be trivially forged.

## Slide 10
Transforming Learning, Research and Working Environments using ICT
1.3 Configuration – Part 3
Key Config Files
  proxy.conf: Define proxy behavior when forwarding requests to other RADIUS servers
realm institition.ac.ke { nostrip }

## Slide 11
Transforming Learning, Research and Working Environments using ICT
1.3 Configuration – Part 3
Key Config Files
  users: Temporary flat file user database for local authentication
  Used for testing or very basic deployments
alice Cleartext-Password := "password123"

## Slide 12
Transforming Learning, Research and Working Environments using ICT
1.4 Testing – Part 1
Finally test that the setup is working. Run freeradius in debug mode
freeradius -XC # check configuration syntax
freeradius -X # run in debug mode

## Slide 13
Transforming Learning, Research and Working Environments using ICT
1.4 Testing – Part 2
In another tab, test that a user is being authenticated. Ma\ke sure that the debug command is still running in another tab freeradius -xX
radtest -t mschap sqltest@institution.ac.ke testpwd localhost 1812 testing123 radtest -t pap sqltest@institution.ac.ke testpwd localhost 1812 testing123 radtest -t chap sqltest@institution.ac.ke testpwd localhost 1812 testing123

## Slide 14
Transforming Learning, Research and Working Environments using ICT
1.4 Testing – Part 3
If it works, you should get an Access-Accept as shown below
rad_recv: Access-Accept packet from host 127.0.0.1 port 1812, id=178, length=20

## Slide 15
Transforming Learning, Research and Working Environments using ICT
1.5 Configuring a Client
Now that the server is working we can configure a client to query the server
We could configure a NAS device if we had one

## Slide 16
Transforming Learning, Research and Working Environments using ICT
1.6 What more could we do?
Store credentials in a database such as mysql, or a directory service such as LDAP so that we could associate additional meta-data about the user with the account
Generate accounting data, so that we could bill for timed access to resources (at a wireless hotspot or a hotel for example)

## Slide 17
Transforming Learning, Research and Working Environments using ICT
Section 2: Integration with LDAP/Active Directory
2.1 Enabling LDAP Module
cd /etc/freeradius/3.0/mods-enabled
ln -s ../mods-available/ldap

## Slide 18
Transforming Learning, Research and Working Environments using ICT
Section 2: Integration with LDAP/Active Directory
2.1 Enabling LDAP Module
cd /etc/freeradius/3.0/mods-enabled
ln -s ../mods-available/ldap

## Slide 19
Transforming Learning, Research and Working Environments using ICT
2.2 Editing LDAP Configuration
Edit mods-available/ldap:
server = 'ldap.example.org'
identity = 'cn=admin,dc=example,dc=org'
password = 'your_password'
base_dn = 'dc=example,dc=org'

## Slide 20
Transforming Learning, Research and Working Environments using ICT
2.3 Test the LDAP Integration
Edit mods-available/ldap:
radtest testuser password localhost 0 testing123

## Slide 21
Transforming Learning, Research and Working Environments using ICT
Bibliography
FreeRADIUS - http://www.freeradius.org/
eduroam https://eduroam.org/

## Slide 22
Transforming Learning, Research and Working Environments using ICT
Section 5: Hand-On Lab
Next session

## Slide 23
www.kenet.or.ke
Jomo Kenyatta Memorial
Library, University of Nairobi
P. O Box 30244-00100, Nairobi.
0732 150 500 / 0703 044 500
Thank You