## Slide 1
Ms. Anne Inapat
Sr. Systems Administrator
KENET
ainapat@kenet.or.ke
Transforming Learning, Research and Working Environments using ICT
Federation Membership and Testing

## Slide 2: eduroam Compliance requirements – Technical
Transforming Learning, Research and Working Environments using ICT
SSID: Must be exactly "eduroam" (case-sensitive)
WPA2/WPA3-Enterprise with IEEE 802.1X
AES (CCMP) encryption; TKIP not allowed
No captive portals (use 802.1X/EAP only)
RADIUS servers configured to proxy requests
Mutual TLS between institutional RADIUS and NRO
Support at least one secure EAP method (EAP-TTLS, PEAP, EAP-TLS)
Usernames in RFC 4282 format: user@institution-domain
Institutional RADIUS must forward unknown realms to NRO

## Slide 3: eduroam Compliance requirements – Security
Transforming Learning, Research and Working Environments using ICT
Use valid, trusted RADIUS server certificates (no self-signed)
Protect credentials: use anonymous outer identity
No shared accounts; personal unique accounts only
Maintain logs for troubleshooting and legal traceability
Logs must include timestamps, MAC, IP, and authentication results

## Slide 4: eduroam Compliance requirements – Policy
Transforming Learning, Research and Working Environments using ICT
Follow global eduroam policy and local NRO rules
Retain logs for required legal period (6 months to 1 year)
Provide support for home users and visiting users
Ensure visiting users can connect without extra registration
Participate in national/global monitoring services

## Slide 5: eduroam Compliance requirements – Summary
Transforming Learning, Research and Working Environments using ICT
To be eduroam-compliant, an institution must:
1. Broadcast 'eduroam' SSID with WPA2/WPA3-Enterprise.
2. Use 802.1X with secure EAP methods.
3. Operate a RADIUS server linked to the NRO/global infrastructure.
4. Protect credentials and maintain logs.
5. Follow national and global eduroam policy guidelines.

## Slide 6: Joining national/regional federations
Transforming Learning, Research and Working Environments using ICT
To join eduroam, follow these steps:
Step 1: Contact KENET (Kenya Education Network), the national eduroam operator in Kenya, to express your interest in joining eduroam.
Step 2: KENET will assess your institution’s readiness and provide initial requirements and documentation.
Step 3: Sign the necessary agreements to formalize your institution’s participation in eduroam.
Configure the server to communicate with the KENET eduroam RADIUS server
Source: www.eduroam.ac.ke
Notes: To join eduroam, your institution needs to become a member of the national eduroam federation (KENET)

## Slide 7: Joining national/regional federations
Transforming Learning, Research and Working Environments using ICT
What are the ongoing responsibilities after joining eduroam?
After joining eduroam, your institution has the following responsibilities:
Maintenance: Regularly maintain and update your RADIUS server and wireless infrastructure.
Support: Provide support to your users and troubleshoot connectivity issues.
Compliance: Ensure compliance with eduroam policies and data protection regulations.

## Slide 8: Using eduroam CAT (Configuration Assistant Tool)
Transforming Learning, Research and Working Environments using ICT
Customised installers developed for organisations to on-board their students and staff onto eduroam.
Eduroam CAT is offered ways for a wide range of different devices (iOS, Android or Windows) to connect to eduroam. However recent changes to the way some operating systems work has meant the CAT alone cannot provide the support needed and so geteduroam was developed.

## Slide 9: Using eduroam CAT (Configuration Assistant Tool)
Transforming Learning, Research and Working Environments using ICT
Android 8 and higher | Windows 8 and newer | MacOS (10.15 or newer) | Linux
Download the eduroam CAT app and get your config from eduroam CAT | Download installer from eduroam CAT | Get a .mobileconfig from eduroam CAT | Get an installation script from eduroam CAT

## Slide 10: Using eduroam CAT (Configuration Assistant Tool)
Transforming Learning, Research and Working Environments using ICT
To use eduroam CAT:
Download the geteduroam app from Google Play or directly via https://www.geteduroam.app
Within the app, search for Institution and select "Institution University > Institution eduroam"
You will then be prompted to enter your credentials in the correct format.

## Slide 11
www.kenet.or.ke
Jomo Kenyatta Memorial
Library, University of Nairobi
P. O Box 30244-00100, Nairobi.
0732 150 500 / 0703 044 500
Thank You