Point to point link LAB

Due to limitation of devices, the lab setup will be done between groups. Each group should have the following:

- One (1) ubiquiti NanoStation 5 Loco

- Three (3) patch codes.

- One (1) poe injector.

Each group needs to identify which group will form point-to-point link with.Remember to always document your settings in a table as below:

|  | Group X | Remote Group Y |
| --- | --- | --- |
| Device Username: |  |  |
| Device Password: |  |  |
| AP ip Address: |  |  |
| AP mode: |  |  |
| SSID: |  |  |
| Channel: |  |  |
| Security: |  |  |
| Ap Mac address: |  |  |

Configure a network interface on one if your computers to have a network interface 192.168.1.8x/24 where x is your group number. Why do you do this?

In the Linux/ubuntu systems this could be done with:

ifconfig eth0:1 192.168.8x/24

Plug power into the first access point (on the nanostation it's the sole ethernet, on the power station it's the one closest to the center).

Plug the lan ethernet jack on the power injector into the PC...

point a web browser at 192.168.1.20

login with:

username

ubnt

password

ubnt

select network:

change the ip address of the device to:

192.168.1.x1

where x is the number of your group.

Go to services

enable the snmp agent

configure the snmp community to be training

go to system

Change the current password from ubnt to trainingx where x is your group number

Set the hostname to apx where x is your group number.

go to link setup

Change the wireless mode from station to access point.

Select a channel.

set your ssid to be wsws-x where x is your group number.

Crank the output power down from 26dBm to 5dBm

Remote  AP

Power on the second ap and repeat the selections except the ip address is going to be 192.168.1.x2

the wireless mode should be set to station

and the hostname should be set to stx where x is your group number

Setup

once all the settings have been applied move both APs to the back of the room