## Slide 1
Transforming Learning, Research and Working Environments using ICT

## Slide 2: IPv4/IPv6 Network Implementation and Operation

## Slide 3: any difference b/w IPv4 and IPv6 ?
Yes, there are, but not significant
  Address architecture
    32bit --> 128bit, you know :)
    vast address space
      don’t worry about subnet mask design any more
      just assign /64 to any subnet
  New routing protocol
    brand new (OSPFv3), improved (RIPng), extension (BGP4+/IS-IS)
Logically separated
  implementing IPv6 won’t affect existing production IPv4 network
    so you can enable IPv6 today
    but in case you need router software upgrade …
IPv6
IPv4
Prefix Length

## Slide 4: Transition/Migration (1) – intro
In one phrase …
It’s easy and stable !
No additional cost (may need software upgrade)
“JUST ENABLE IT !!”

## Slide 5: Transition/Migration (2) – intro
… some more words
  assign IPv6 address to all interfaces where IPv4 address is assigned
  launch your favorite IPv6 routing protocols
    BGP4+
    IS-IS / OSPFv3
    even RIPng, static
Principle (from my experience)
  “Keep It Simple”
    make all routers/services dual stack
      there should be gradual steps, but try to make it short
    make IPv6 design the same as IPv4 design
      follow the same physical design as IPv4
        better not use logical overlay (ex. tunnel, VLAN, MPLS)
  this will reduce training/operational costs

## Slide 6: Transition/Migration (3) – Practice
Transition Strategy
  Physically different IPv6 network
  Tunnel (IP tunnel, MPLS)
  various translation mechanisms (ISATAP, 6to4, Teredo …)
  Dual Stack
Migration Plan
  Addressing Design
  Routing Design
  Operation Design
Preparation
  Operator training
    though, it’s just a textual representation difference
  DNS
    IPv6 (AAAA, PTR) record registration
  Operation tools
    ping, traceroute, internal tools upgrade (to support IPv6)
it’s hard to make IPv6 only node even using transition technologies
cost
logical overlay

## Slide 7: Transition (1)
IPv6 Internet
IPv6 Internet
IPv4 only core
IPv4 only router
IPv4/IPv6 dual stack router
IPv4 only link
IPv6 only link
IPv4/IPv6 link
IPv6 Customer
IPv4 Customer
IPv6 over IPv4 tunnel
core
edge
edge
for IPv6
customers only
IPv4 Customer
IPv4 Customer
only edge router is dual stack
You may skip this step
example

## Slide 8: Transition (2)
IPv6 Internet
IPv6 Internet
dual stack in the core
IPv4 only router
IPv4/IPv6 dual stack router
IPv4 only link
IPv6 only link
IPv4/IPv6 link
IPv6 Customer
IPv4 Customer
IPv6 over IPv4 tunnel
core
edge
edge
IPv4 Customer
IPv4 Customer
some routers are still IPv4 only
example

## Slide 9: Transition (3)
IPv6 Internet
IPv6 Internet
IPv4 only router
IPv4/IPv6 dual stack router
IPv4 only link
IPv6 only link
IPv4/IPv6 link
IPv4/IPv6 Customer
IPv4 Customer
core
edge
edge
IPv4/IPv6 Customer
IPv6 Customer
dual stack to the edge
example

## Slide 10: Migration Plans
Transition Strategy
  Physically different IPv6 network
  Tunnel (IP tunnel, MPLS)
  various translation mechanisms (ISATAP, 6to4, Teredo …)
  Dual Stack
Migration Plan
  Addressing Design
  Routing Design
  Operation Design
Preparation
  Operator training
    though, it’s just a textual representation difference
  DNS
    IPv6 (AAAA, PTR) record registration
  Operation tools
    ping, traceroute, internal tools upgrade (to support IPv6)

## Slide 11: IPv6 Address
needs IPv6 address ? - contact your NIR or RIR
  it’s not hard to get IPv6 address block if you’re running IPv4 network already
will be able to assign IPv6 address in more tidy way
  IPv4
    it’s hard to get “one big block”
    need to use fractions of prefixes
  IPv6
    you can get “big” IPv6 block
    easy to make your own addressing architecture
IPv4
IPv6

## Slide 12: Addressing Design (1)
Design addressing in structured manner
  though we know it will become ad-hoc some day …
Assign enough address block per POP basis
  use the same assignment design in each POP
  easy to make ACL
  easy to understand from which block to assign new address
  easy to aggregate
/48
/48
/48
/48
/48
/48
POP1
POP2
POP3
loopback
p-t-p
switch
server
customer
reserved
/32
/34
/34
/34
/48
example

## Slide 13: Addressing Design (2)
p-t-p link address assignment
  /64 will be good, some use /126 (just like IPv4)
    don’t hesitate to waste addresses
    keep it clean and simple
Not recommended
  you’d better not assign EUI-64 based address
    2001:db8:0:d802:2d0:b7ff:fe88:eb8a
  don’t try to make complex rules
    2001:db8:[POP ID]:[POP ID]:[Service ID]::XX
in IPv4, usually /30 or /31 is assigned
example

## Slide 14: Routing Design (1)
BGP
  Separate IPv6 peering from IPv4 peering
    You can minimize IPv6 deployment impact on IPv4 network
  Again, try to use the same routing policy for both sessions
    if there is no protocol dependent configuration in routing policy (ex. “route-map”), you’d better use it for both protocols
IPv4 peering for IPv4 routing
IPv6 peering for IPv6 routing
BGP router
BGP router
IPv4 peer config
IPv6 peer config
IPv6 dependent policy
IPv4 dependent policy
protocol independent policy

## Slide 15: Routing Design (2)
OSPFv2 (for IPv4) and OSPFv3 (for IPv6)
  completely different protocol
  co-exist
    does not affect each other
    easy to deploy IPv6 (OSPFv3) gradually
IS-IS
  single topology for IPv4 and IPv6
    though there is multi-topology extension
  (w/o extension above) need X-day
    to enable IPv6, all IS-IS nodes have to enable IPv6 at the same time. difficult to deploy gradually.
Better use the same protocol as in IPv4

## Slide 16: Operation Design (1)
Monitoring
  traffic grapher usually counts L2 byte counter
    not many routers support IPv6 MIB
      unable to count IPv6 only traffic
  only a few routers support IPv6 SNMP transport
    routers still have to have IPv4 connectivity
  not many NMS support IPv6
    in case supported, usually need upgrade
Accounting
  as written above, routers/accounting system usually cannot count IPv6 bytes only
  thus, cannot charge IPv4/IPv6 traffic separately
count only sum of bytes
ISP
Customer

## Slide 17: Operation Design (2) (or “tips”)
Router operation
  command output may be slightly different depends on router platform
  default protocol for commands (ping, traceroute, telnet …) will become IPv6
  don’t forget to set ACL for IPv6
Server operation
  default protocol for commands, again, become IPv6
    need to specify protocol explicitly sometimes (ex. “-4”)
  don’t forget to setup firewall for IPv6
    though not many firewall vendor support IPv6

## Slide 18: Access Network Service (1)
Dual stack service
  users will be assigned /48
  need auto prefix assignment protocol
    “Prefix Delegation protocol”
Tunnel service
  easy to deploy
  hard to support edge devices
IPv4 service
Tunnel service
Dual stack service
misc.

## Slide 19: Access Network Service (2)
Protocols for dual stack service
  running since 2002
  nation wide service via L2TP in Japan
ISP
ADSL
LAN
PPP (IPv6CP)
Stateless Address
Auto Configuration
assign /48 to home network
Home router
Home router will announce /64 out of assigned /48 through Router Advertisement
misc.
DHCPv6-PD

## Slide 20
Seiji Ariga NTT Communications

## Slide 21: IPv6 Now
IPv6 address allocation
  around 250 prefixes per year are allocated since 2003
    now 1397 prefixes have been allocated
  not all of them are visible on the net
  cf. http://www.ripe.net/rs/ipv6/stats/
  http://www.sixxs.net/tools/grh/dfp/
routing table
  IPv4: < 170,000 routes
  IPv6: < 600 routes
    IPv6 has “Aggregatable Addressing Architecture” :)
applications
  a lot of UNIX applications are IPv4/IPv6 capable
  WindowsXP has IPv6 functionality (and Vista may have more)
    Internet Explorer, Firefox, MSN Messenger, and more

## Slide 22: IPv6 Now : ex. NTT Communications Global IP Network
We’re running IPv4/IPv6 native dual stack network since 2003
  all routers are fully dual stack
  connects to both IPv4 only, IPv6 only, IPv4/IPv6 IX
  provides IPv4, IPv6, IPv4/IPv6 services all over the world
some servers also provide IPv4/IPv6 service
NSPIXP6
PAIX
AMS-IX
LINX
UK6X
JPNAP6
EQUI6IX
Japan
Korea
Taiwan
Hong Kong
Malaysia
Australia
U.S.
Europe
DE-CIX
PARIX
EQUI6IX
ESPANIX
HK6IX
IPv6 IX

## Slide 23: any difference b/w IPv4 and IPv6 ?
Yes, there are, but not significant
  Address architecture
    32bit --> 128bit, you know :)
    vast address space
      don’t worry about subnet mask design any more
      just assign /64 to any subnet
  New routing protocol
    brand new (OSPFv3), improved (RIPng), extension (BGP4+/IS-IS)
Logically separated
  implementing IPv6 won’t affect existing production IPv4 network
    so you can enable IPv6 today
    but in case you need router software upgrade …
IPv6
IPv4
Prefix Length

## Slide 24: Transition/Migration (1) – intro
In one phrase …
It’s easy and stable !
No additional cost (may need software upgrade)
“JUST ENABLE IT !!”

## Slide 25: Transition/Migration (2) – intro
… some more words
  assign IPv6 address to all interfaces where IPv4 address is assigned
  launch your favorite IPv6 routing protocols
    BGP4+
    IS-IS / OSPFv3
    even RIPng, static
Principle “Keep It Simple”
    make all routers/services dual stack there should be gradual steps, but try to make it short
    make IPv6 design the same as IPv4 design follow the same physical design as IPv4
        better not use logical overlay (ex. tunnel, VLAN, MPLS)
  this will reduce training/operational costs

## Slide 26: Transition/Migration (3) – Practice
Transition Strategy
  Physically different IPv6 network
  Tunnel (IP tunnel, MPLS)
  various translation mechanisms (ISATAP, 6to4, Teredo …)
  Dual Stack
Migration Plan
  Addressing Design
  Routing Design
  Operation Design
Preparation
  Operator training
    though, it’s just a textual representation difference
  DNS
    IPv6 (AAAA, PTR) record registration
  Operation tools
    ping, traceroute, internal tools upgrade (to support IPv6)
it’s hard to make IPv6 only node even using transition technologies
cost
logical overlay

## Slide 27: Transition (1)
IPv6 Internet
IPv6 Internet
IPv4 only core
IPv4 only router
IPv4/IPv6 dual stack router
IPv4 only link
IPv6 only link
IPv4/IPv6 link
IPv6 Customer
IPv4 Customer
IPv6 over IPv4 tunnel
core
edge
edge
for IPv6
customers only
IPv4 Customer
IPv4 Customer
only edge router is dual stack
You may skip this step
example

## Slide 28: Transition (2)
IPv6 Internet
IPv6 Internet
dual stack in the core
IPv4 only router
IPv4/IPv6 dual stack router
IPv4 only link
IPv6 only link
IPv4/IPv6 link
IPv6 Customer
IPv4 Customer
IPv6 over IPv4 tunnel
core
edge
edge
IPv4 Customer
IPv4 Customer
some routers are still IPv4 only
example

## Slide 29: Transition (3)
IPv6 Internet
IPv6 Internet
IPv4 only router
IPv4/IPv6 dual stack router
IPv4 only link
IPv6 only link
IPv4/IPv6 link
IPv4/IPv6 Customer
IPv4 Customer
core
edge
edge
IPv4/IPv6 Customer
IPv6 Customer
dual stack to the edge
example

## Slide 30: Migration Plans
Transition Strategy
  Physically different IPv6 network
  Tunnel (IP tunnel, MPLS)
  various translation mechanisms (ISATAP, 6to4, Teredo …)
  Dual Stack
Migration Plan
  Addressing Design
  Routing Design
  Operation Design
Preparation
  Operator training
    though, it’s just a textual representation difference
  DNS
    IPv6 (AAAA, PTR) record registration
  Operation tools
    ping, traceroute, internal tools upgrade (to support IPv6)

## Slide 31: IPv6 Address
needs IPv6 address ? - contact your NIR or RIR
  it’s not hard to get IPv6 address block if you’re running IPv4 network already
will be able to assign IPv6 address in more tidy way
  IPv4
    it’s hard to get “one big block”
    need to use fractions of prefixes
  IPv6
    you can get “big” IPv6 block
    easy to make your own addressing architecture
IPv4
IPv6

## Slide 32: Addressing Design (1)
Design addressing in structured manner
  though we know it will become ad-hoc some day …
Assign enough address block per POP basis
  use the same assignment design in each POP
  easy to make ACL
  easy to understand from which block to assign new address
  easy to aggregate
/48
/48
/48
/48
/48
/48
POP1
POP2
POP3
loopback
p-t-p
switch
server
customer
reserved
/32
/34
/34
/34
/48
example

## Slide 33: Addressing Design (2)
p-t-p link address assignment
  /64 will be good, some use /126 (just like IPv4)
    don’t hesitate to waste addresses
    keep it clean and simple
Not recommended
  you’d better not assign EUI-64 based address
    2001:db8:0:d802:2d0:b7ff:fe88:eb8a
  don’t try to make complex rules
    2001:db8:[POP ID]:[POP ID]:[Service ID]::XX
in IPv4, usually /30 or /31 is assigned
example

## Slide 34: Routing Design (1)
BGP
  Separate IPv6 peering from IPv4 peering
    You can minimize IPv6 deployment impact on IPv4 network
  Again, try to use the same routing policy for both sessions
    if there is no protocol dependent configuration in routing policy (ex. “route-map”), you’d better use it for both protocols
IPv4 peering for IPv4 routing
IPv6 peering for IPv6 routing
BGP router
BGP router
IPv4 peer config
IPv6 peer config
IPv6 dependent policy
IPv4 dependent policy
protocol independent policy

## Slide 35: Routing Design (2)
OSPFv2 (for IPv4) and OSPFv3 (for IPv6)
  completely different protocol
  co-exist
    does not affect each other
    easy to deploy IPv6 (OSPFv3) gradually
IS-IS
  single topology for IPv4 and IPv6
    though there is multi-topology extension
  (w/o extension above) need X-day
    to enable IPv6, all IS-IS nodes have to enable IPv6 at the same time. difficult to deploy gradually.
Better use the same protocol as in IPv4

## Slide 36: Operation Design (1)
Monitoring
  traffic grapher usually counts L2 byte counter
    not many routers support IPv6 MIB
      unable to count IPv6 only traffic
  only a few routers support IPv6 SNMP transport
    routers still have to have IPv4 connectivity
  not many NMS support IPv6
    in case supported, usually need upgrade
Accounting
  as written above, routers/accounting system usually cannot count IPv6 bytes only
  thus, cannot charge IPv4/IPv6 traffic separately
count only sum of bytes
ISP
Customer

## Slide 37: Operation Design (2) (or “tips”)
Router operation
  command output may be slightly different depends on router platform
  default protocol for commands (ping, traceroute, telnet …) will become IPv6
  don’t forget to set ACL for IPv6
Server operation
  default protocol for commands, again, become IPv6
    need to specify protocol explicitly sometimes (ex. “-4”)
  don’t forget to setup firewall for IPv6
    though not many firewall vendor support IPv6

## Slide 38: Access Network Service (1)
Dual stack service
  users will be assigned /48
  need auto prefix assignment protocol
    “Prefix Delegation protocol”
Tunnel service
  easy to deploy
  hard to support edge devices
IPv4 service
Tunnel service
Dual stack service
misc.

## Slide 39: Access Network Service (2)
Protocols for dual stack service
  running since 2002
  nation wide service via L2TP in Japan
ISP
ADSL
LAN
PPP (IPv6CP)
Stateless Address
Auto Configuration
assign /48 to home network
Home router
Home router will announce /64 out of assigned /48 through Router Advertisement
misc.
DHCPv6-PD

## Slide 40
Transforming Learning, Research and Working Environments using ICT
Attributed to Seiji Ariga
NTT Communications

## Slide 41
www.kenet.or.ke
Jomo Kenyatta Memorial
Library, University of Nairobi
P. O Box 30244-00100, Nairobi.
0732 150 500 / 0703 044 500
Thank You